## Slide 1: Enhancing Condition Monitoring of Mining Vehicles Using Physical Models and Transfer Learning
Presenter: Luke van Eyk
Supervisors: Prof PS Heyns, Dr S Schmidt
Centre for Asset Integrity Management (C-AIM)
University of Pretoria

## Slide 2: Context
Digitization = Instrumented fleets
Large amount of operational data being captured
How can we use this data to determine useful KPIs?
These KPIs are typically difficult/impossible to measure in real time:
  Fuel usage - Production
  Engine temperature – Condition monitoring (Today’s focus)
  LHD Bucket load/volume
  etc.
How would such correlations typically be done?
Notes: Key here is that we want real time feedback!

## Slide 3: Common supervised learning framework:
Machine KPI Prediction
Real data + labels
Feature Extractor
Features
Label predictor
Very few or ZERO labels!
Engine Temp: 400 K
Fuel Usage:
0.1 l/min
Load hauled:
4.5 tons
Notes: Our “knowledge” comes from a few labelled samples
Or we don’t have any knowledge if we don’t have labelled data
Can we use existing data to determine some “harder” quantities, without necessarily having their labels? Thus regression without sensors. ;

## Slide 4: Current problem
We can see that these supervised methods rely on labels
We don’t have labels
What can we do?
  Part 1: Hybrid model for data generation/training
  Part 2: Transfer learning for model calibration

## Slide 5: A hybrid methodology:
Physical reality (Machine)
Known physics
Unknown physics
Data
Physics-driven model
Data-driven model
Hybrid model
Decision-making
Notes: In this sense, we hope that the data can capture elements of the physical reality that our physical model could not.

## Slide 6: Hybrid model for diagnosis
Data-Driven
Physics-Driven
Hybrid
Increasing Labelled Data
Increasing Predictive Accuracy
Conceptualisation
Data-Driven
Physics-Driven
Hybrid

## Slide 7: Proposed hybrid approach
Simulated data
Feature Extractor
Features
Label predictor
Physics-driven
Data-driven
Hybrid
Machine KPI Prediction
Engine Temp: 400 K
Fuel Usage:
0.1 l/min
Load hauled:
4.5 tons
Notes: Here our knowledge comes from the simulations.

## Slide 8: Shortcoming of this method
?
Numerical/Training Data
Alternate/Real Data
Contains some useful information about the system, but calibrated to input data
Data-driven
Data-driven
Hard divide
Machine KPI prediction
Machine KPI prediction
Notes: The simulation-trained ML model will not necessarily generalize well to data from the real/similar asset
May not even generalize within the same asset for different operating conditions!
We have, however, learnt some useful info from numerical data
How do we “transfer” this info to a ML model which receives a different input dataset?

## Slide 9: Solution: Transfer learning
Data-driven
Data-driven
Transfer information
Source Domain
Target Domain
Machine KPI prediction
Notes: Transfer learning is a field of machine learning focused on tackling exactly this problem:
  How do we transfer knowledge from one domain of data to another.
Some terminology:
  Source domain
    Domain on which initial model was trained.
    We have lots of data + labels.
    Model mainly trains on this data
  Target domain:
    Domain in which model is to be applied
    We have data but very few or no label

## Slide 10: Transfer learning structure
Machine KPI Prediction
Source data
Feature Extractor
Features
Label predictor
Target data
Source
Target
Compare and penalize if not similar
Joint Task
Notes: The following structure is used to transfer knowledge:
Model is jointly incentivized to produce similar feature distributions, regardless of input domain
Model is also incentivized to produce accurate labels from the features it receives.
Labels only need to be available for source domain.
Can still pass labels for target domain if available – Power of this technique

## Slide 11: Investigation of transfer learning utility
Vehicle Vibrations
Throttle Position
Engine RPM
Engaged Gear no.
Fuel Flow Rate
Vehicle Vibrations
Throttle Position
Engine RPM
Engaged Gear no.
Fuel Flow Rate
Engine exhaust manifold temperature prediction
Data-driven model
Engine exhaust manifold temperature prediction
Data-driven model
Fleet
Transfer learning calibration
Simulated vehicle
Real vehicle with limited instrumentation
Known during training
Hidden during training

## Slide 12: Numerical study on vehicle:
Notes: I don’t have time to go into detail, but in this study, I simulated a vehicle in Matlab
As input to the hybrid framework model, I simulated:
Vibrations
Throttle position
Engine RPM
Current gear
Fuel flow rate
As output, I tried to predict the engine exhaust temperature.
I have a different source and target domain
Note that this is for a car, but the concept quite easily extends to mining vehicles.

## Slide 13: Numerical study on vehicle
Input data:
Vehicle Vibrations
Throttle Position
Engine RPM
Engaged Gear no.
Fuel Flow Rate
Data-driven model
Engine exhaust manifold temperature prediction
Notes: I don’t have time to go into detail, but in this study, I simulated a vehicle in Matlab
As input to the hybrid framework model, I simulated:
Vibrations
Throttle position
Engine RPM
Current gear
Fuel flow rate
As output, I tried to predict the engine exhaust temperature.
I have a different source and target domain
Perhaps expand on the fact that for the target domain,

## Slide 14: Domains
Source domain: Simulated vehicle with engine temperature known to data-driven model
Target domain: Different simulated vehicle without engine temperature known to model

## Slide 15: Source domain (temperatures known)
Source domain
Exhaust Temperature
(Standardised)
Good results because we have labels

## Slide 16: Results: Engine temperature predictions for unseen vehicle
Prediction
Truth
Prediction
Truth
Target (No calibration)
Exhaust Temperature
(Standardised)
Exhaust Temperature
(Standardised)
Remember we have no labels for training. Only raw sensor data (no temperature data as reference)
Target (Calibrated by transfer learning)
Notes: Over the range of temperature predictions, we sorted them from small to large and evaluated the accuracy of the non-transfer vs. transfer method.
Clearly there is a benefit to transfer-learning.
Important to remember we did not have this regressive information during training. We only have the relationships between inputs and outputs of SOURCE domain and infer the relevant mapping to the target domain.

## Slide 17: Conclusions
Hybrid methods allow us to:
  Model known physics
  Infer unknown physics
  Use knowledge from both
However, they suffer when target data differs from source
Transfer learning helps us calibrate for these differences
Hybrid + Transfer is a recipe for exciting diagnostic potential

## Slide 18: Applications
Simulate a vehicle (with labels) and transfer to real vehicle (with no labels)
Take a vehicle full of sensors and transfer knowledge to unknown vehicle
Or fleet
This engine temperature example:
  Virtual sensor
  Anomaly detection sensor

## Slide 19: Thank you
Any questions or comments are welcome
Contact details:
Luke.vaneyk@up.ac.za